# Zusammenfassung FEM II

In which equation is the material response given?
Constitutive equations

What does the material model define?
The stress response in term sof the history of the strains

What is simplest class of material models?
Stresses and strains are both local quantities

What is an example for a material model?
Standard linear elasticity

What is the difference between elastic and inelastic response?
- Elastic response is independent of the history
- Inelastic not

What are examples of the inelastic responses?
- perfectly plastic behavior
- linear plastic hardening
- rate-dependent / visco-elastic

Which are the six global equations the thermodynamic framework?
- Conservation of mass
- Conservation of linear momentum
- Kinetic energy
- Internal energy
- Entropy
- Entropy production

What is the definition of linear momentum?
- The momentum is the result of the multiplication of the body‘s mass and velocity
- linear momentum refers to translational movement

What is heat?
Total energy of molecular motion

What is temperature?
Measure of the average energy of molecular motion

The continuum is loaded by mechanical and thermal processes. Which are the four resulting loadings?
- Mechanical force
- Mechanical power
- Thermal power
- Entropy power

Which are the global balance laws of thermodynamics?
- Conservation of mass
- Conservation of linear momentum
- Conservation of total energy (1st law of thermodynamics)
- Entropy (2nd law of thermodynamics)

What does the law of the Conservation of Total Energy say?
The change of total energy equals the sum of the mechanical and thermal power acting on the body

How are the local balance laws obtained from the global ones?
By making the finite subvolume P become infinitesimally small

What does thermodynamically consistent mean?
The fourth global law is fulfilled (2nd law of thermodynamics)

What is the Clausius-Duhem inequality?
A formulation of the 2nd law of thermodynamics which is used for continuum mechanics

What does it say?
Entropy varies with temperature but it never decreases in an isolated system

What does irreversibility mean?

What is thermodynamic equilibrium?
The system does not evolve over time

What is a thermodynamic state?
Values that provide all information needed to characterize the system (e.g. stress, strain, velocity, temperature, etc.)

What is a thermodynamic process?
Transition from onr thermodynamic state to another

What is the definition of entropy?

We only have four equations so far but seven unknown variables. How do we solve this problem?
By introducing constitutive equations

What are the rules and principles for constitutive equations?
- Principle of determinism
- Principle of frame indifference
- Principle of physical consistency
- Principle of local action (simplest case)

What does the principle of determinism say?
If we know all information about a material at a certain time we know exactly how it will evolve in future

What does the principle of frame indifference say?
The constitutive equations must also be valid if we change the coordinate system (the observer)

What does the principle pf physical consistency say?
The constitutive equations cannot violate or contradict the global balance laws of thermodynamics

What does the principle of local action say?
- The dependent constitutive variables at X are only dependent of independent variables which are also located at X
- not valid for e.g. gradient plasticity

What is dissipation?
A result of an irreversible thermodynamic process

Which two inequalities can be derived from the Clausius-Duhem inequality?
- Clausius-Planck inequality
- Fourier inequality

What is the Coleman‘s exploitation method?
Formulating constitutive equations for thermo-elasticity which are thermodynamically consistent and in the end only depend on two variables

Which energy serves as a potential for the stress and the entropy?
Helmholtz free energy

In thermo-elasticity it is sufficient to prescribe which parameters?
- The Helmholtz free energy and the heat flux
- everything else can be derived from these two values